## Slide 1
!
PPT No. 6 | COMMUNITY SERVICE PROJECT
Burglar / Intruder / Theft
Door Alarm with Buzzer
DEPARTMENT
CSE (AI & ML)
SECTION
B
GROUP NO.
6
GUIDE
Mr. B. Venkateswara Reddy
TEAM MEMBERS
24BQ1A4288 D. Venkata Siva Prasad
24BQ1A42B9 G. Mahesh Reddy
24BQ1A42B7 G. Yedukondalu
Burglar / Intruder / Theft Door Alarm with Buzzer
1

## Slide 2
Problem Statement & Introduction
PROBLEM STATEMENT
Burglary and unauthorized entry are common security concerns. Traditional locks alone give no immediate warning. A low-cost electronic alarm can alert people the moment an intruder attempts to enter.
•
Risk of burglary in homes & rural areas
•
Lack of affordable security systems
•
Need for immediate, audible alerts
•
Need for easy installation & maintenance
INTRODUCTION
The project uses sensors to detect unauthorized door entry
An Arduino Nano processes the sensor signal
A buzzer produces a loud audible alarm when intrusion is detected
The result is a simple, low-cost security system anyone can build
A door sensor and motion sensor work together with Arduino to instantly flag unauthorized access.
Burglar / Intruder / Theft Door Alarm with Buzzer
2

## Slide 3
Objectives & Components
OBJECTIVES
1
Detect unauthorized door opening
2
Detect intruder movement
3
Activate an alarm immediately
4
Provide a low-cost security solution
5
Keep the system simple & easy to maintain
MAIN COMPONENTS
Arduino Nano
Processes sensor signals
Magnetic Reed Switch
Detects door opening
PIR Motion Sensor
Detects intruder movement
Relay Module
Switches the buzzer circuit
Buzzer
Sounds the audible alarm
Battery / Power Supply
Powers the whole circuit
Burglar / Intruder / Theft Door Alarm with Buzzer
3

## Slide 4
Circuit Diagram
Door Sensor + PIR Sensor → Arduino Nano → Relay Module → Buzzer
ARDUINO NANO
USB
D2
D3
D8
GND
VIN/5V
Door Sensor
(Magnetic Reed Switch)
PIR Motion Sensor
(Detects movement)
Relay Module
Buzzer
Battery /
Power Supply
Common GND Rail
Signal wire
Power (+)
Ground (GND)
Reed switch (D2) & PIR sensor (D3) send signals to Arduino → Arduino drives relay (D8) → relay switches buzzer ON.
Burglar / Intruder / Theft Door Alarm with Buzzer
4

## Slide 5
Burglar / Intruder / Theft Door Alarm with Buzzer
5

## Slide 6
Advantages, Applications & Future Scope
ADVANTAGES
✓
Low cost
✓
Easy to install
✓
Simple operation
✓
Immediate audible alert
✓
Low power consumption
✓
Easy maintenance
APPLICATIONS
Houses
Shops
Offices
Classrooms
Small warehouses
Storage rooms
FUTURE SCOPE
→ GSM/SMS alerts
→ Wi-Fi / IoT connectivity
→ Mobile application
→ Camera integration
→ Cloud monitoring
→ Solar power
Burglar / Intruder / Theft Door Alarm with Buzzer
6

## Slide 7
Expected Outcomes & Conclusion
EXPECTED OUTCOMES
✓
Detect unauthorized entry
✓
Generate an immediate buzzer alert
✓
Improve awareness of intrusion
✓
Provide an affordable security system
CONCLUSION
The Burglar / Intruder / Theft Door Alarm with Buzzer provides a simple, affordable and effective first level of protection against unauthorized entry, easy to implement for homes and small establishments.
THANK YOU
GUIDE
Mr. B. Venkateswara Reddy
CSE (AI & ML) | Sec B | Group 6
TEAM MEMBERS
24BQ1A4288
D. Venkata Siva Prasad
24BQ1A42B9
G. Mahesh Reddy
24BQ1A42B7
G. Yedukondalu
Burglar / Intruder / Theft Door Alarm with Buzzer
7